## Slide 1: System Identification
CSE 421 Digital Control
Lecture 11

## Slide 2: Introduction
In order to be able to design a controller for a dynamic system, we must have a model of the system describing its dynamic behavior.
In principle, there are two approaches to ﬁnding the model: physical modeling and system identification.
Physical modeling is analytical approach in which basic principles (laws of motion, electrical laws, …) are used to obtains diﬀerential equations describing system behavior.
While this is useful in gaining insight into system behavior, actual physical phenomena may be too complex to permit satisfactory description using physical principles.

## Slide 3: System identification
When physical modeling is not feasible, we may resort to the experimental approach called system identiﬁcation.
In this approach, we first excite the plant with some input sequence, u(0), u(1),…, u(N), and record the corresponding output response, y(0), y(1),…, y(N). Then, we construct a model from this observed data.
In these slides, a brief introduction to system identiﬁcation using the least squares method is presented.

## Slide 4: Worked example
Consider the following first-order model:
  There are two unknown parameters a and b.
The model can be rewritten as a difference equation:
  A feed-forward term u(k) was not included because it is virtually never seen in a physical system (unlike a controller).

## Slide 5
Using the input-output sequences, we can write the following equations:
These are N equations in 2 unknown a and b.
As the number of equations > number of unknowns, there is no value for a and b to satisfy exactly all equations (this is called an over-determined system of equations).

## Slide 6
To deal with this issue, let us insert additional term ε(i) in each equation to account for noise and modeling error.
This set of equations can be written in matrix form:

## Slide 7: Finding the parameters a and b
What we are looking for is a value for θ (i.e. a and b) which makes the best compromise between all the equations, i.e. try to minimize the equation errors ε(1), ε(2),…, ε(N).
One possibility is to choose a and b that make the sum of all errors minimum. That is, to minimize:
However, this is not a good choice. Why?

## Slide 8
To penalize both positive and negative errors ε(i), we seek θ that makes the sum of squared errors minimum. That is,
This leads to the well-known least-squares problem, for which the following estimate can be obtained:

## Slide 9: Example 1
Consider the following model
where u(k), y(k), and ε(k) are, respectively, the input, output, and the equation error at time instant k. Given the following input output data:
  deduce the regression matrix Φ
  calculate the least squares estimate of a and b.
  calculate the model output
  calculate the residuals
t | 1 | 2 | 3 | 4 | 5
u(t) | 1 | 2 | 4 | 5 | 7
y(t) | 1 | 3 | 5 | 7 | 8

## Slide 10: Answer
We can write:

## Slide 11
Hence, the least squares estimate is given as:

## Slide 12
Using the estimate of a and b, the model output is given by
Hence the residuals are

## Slide 13: Example 2
Consider the following model
where y(k) is the system output at instant k and e(k) is an equation error. Given the following input output data,
  deduce the regression matrix Φ
  calculate the least squares estimate of a and b.
  calculate the model output
  calculate the residuals
t | 1 | 2 | 3 | 4 | 5
u(t) | 1 | 2 | 4 | 5 | 7
y(t) | 1 | 3 | 5 | 7 | 8

## Slide 14: Answer
We can write:

## Slide 15
Hence, the least squares estimate is:
Using the estimate of a and b, the model output is
Hence the residuals are