## Slide 1: State Space Representation

## Slide 2: State space representation
While transfer functions are used to model dynamic systems in the frequency domain, state space representation is a way of modelling systems in the time domain.
Time domain is suitable for software implementation.
  Non-zero initial conditions can be treated easily.
  The number of inputs or outputs does not affect the complexity of the equations.

## Slide 3: State space representation
An nth order differential equation can be decomposed into n first-order equations by introducing new variables called the state.
The knowledge of the state variables at some initial time, plus knowledge of the input from that time on, is suﬃcient to predict the system behavior.
The State Space is an n-dimensional space in which the components of the state vector represents its coordinate axes.

## Slide 4: State space equations
Input
Output
State
System Matrix
Input Matrix
Output Matrix (lxn)
Feed forward Matrix. Usually D is zero for physical systems.
Where,

## Slide 5: State space description
Variables with which initial conditions are necessary are by deﬁnition state variables.
In mechanical systems: position and velocity
In electrical systems: voltage and current
Any linear combination of state variables is itself a valid state variable. There are inﬁnite number of choices.

## Slide 6: Example
Consider the spring-mass-damper system shown below. The input is the applied force u(t) and the output is the displacement y(t) measured from equilibrium position in the absence of the external force. The equation of motion for this system is
Let m = 1, b = 2, and k = 3.
This system is of second order. Position and velocity are valid state variables, hence, let us define state variables x1(t) and x2(t) as

## Slide 7
Then we obtain
The output equation is
In a vector-matrix form,

## Slide 8: Transfer function from state-space
State space and transfer function are two different, but equivalent, representations of the system. It is possible to convert from one form to the other.
Given the state space description of a system, its transfer function is obtained as:
MATLAB commands to convert between state space and transfer function
>>[num,den] = ss2tf(A,B,C,D)
>>[A,B,C,D] = tf2ss(num,den);

## Slide 9: Example 2
A state space description of a spring-mass-damper system is given by the following matrices:
Find the system transfer function.
Answer: