## Slide 1: System Structures
CSE 425 Industrial Process Control
Lecture 4
Copyright © Thomas Marlin 2013

## Slide 2
Simple dynamic elements can yield complex dynamics when combined in typical process structures.
Series
Parallel
Recycle
Process Structures

## Slide 3: Systems in Series
Examples:
The transfer function between inlet flow qi to 2nd tank level is 2nd order.
T
T
Interacting series:
Flow between tanks depends on level in 2nd tank.
Non-interacting series:
Flow between tanks doesn’t depend on level in 2nd tank.
qi
qi

## Slide 4
Gvalve(s)
Gtank2(s)
Gtank1(s)
Gsensor(s)
v(s)
F0(s)
T1(s)
T2(s)
Tmeas(s)
The block diagram of a non-interacting series is:
The transfer function of the series is:
Non-interacting Series

## Slide 5: Multi-capacity processes
If each element in the series is first order, the series is called multicapacity process:
The overall gain is product of gains of each element.
The series is slower (more sluggish) than any single element. The more tanks we have in a series, the longer we have to wait until the last tank “sees” the changes that we have made in the ﬁrst one.

## Slide 6: Numerical Example
Assume that all stages in a multi-capacity process have the same time constant, then the whole system can be modeled as
Let us simulate this system for n = 1, 2, 3, 4, 5.
The response becomes more sluggish as the number of elements in the series increases.
tau = 3;
G = tf(1,[tau 1]);
step(G);
hold
step(G*G);
step(G*G*G);
step(G*G*G*G);
step(G*G*G*G*G);

## Slide 7: Approximation of high-order processes
In the previous figure, the initial response is small and can be ignored. This can be represented with pure dead time.
In practice, high-order processes can be well approximated with ﬁrst-order process plus dead-time (FOPDT):
For example, consider the following 4th order system:

## Slide 8
The response of this system is dominated by the largest time constant 3 (dominant pole at -1/3).
Accordingly, we may approximate the full-order function as
where 1.6 is the sum of the smaller time constants 0.1, 0.5, and 1.
As shown, the approximation is reasonable for t large enough so that the pole at − 1/3 can indeed be considered dominant.

## Slide 9
Sketch the step response for the system below.
 = 2
 = 2
 = 2
 = 2
Step
Class Exercise:

## Slide 10: Parallel Structures
Parallel structures result when there are two paths between input and output, e.g. a flow split, where the paths have different time constants.
G1(s)
G2(s)
U(s)
Y(s)
A  B  C
Example process systems
Block diagram

## Slide 11: Transfer Function of a Parallel Structure
Assume that both elements in parallel are first order, then the overall model is
Combining both terms gives a second-order function with a zero
Where
As we know, the inherent dynamics is governed by the poles, however, the zeros have interesting effects on the response.

## Slide 12: Example
Let us compare the response of three systems:
Which would be
difficult
to control?

## Slide 13: Example
Inverse response (e.g. in G3) is caused by two competing processes – the faster of which takes the process first in a direction opposite to the steady state.
Parallel structures can experience complex dynamics due to the presence of zeros and this may be difficult to control.

## Slide 14: Recycle Structures
Recycle structures result from recovery of material and energy. They are essential for profitable operation.
They strongly affect dynamics. Recycle can be considered analogous to a positive feedback mechanism and thus can make stable processes unstable.
Systems with recycle have longer response time (larger time constants).

## Slide 15
H1(s)
G(s)
H2(s)
Y0(s)
Y(s)
Example
Determine the effect of recycle on the dynamics of the given chemical reactor (faster or slower)? and the overall steady state gain.
+
+

## Slide 16: Mason’s gain formula
System determinant | Δ = 1 – Σ Li + Σ LiLj - Σ LiLjLk + …
Forward path gain | Fi = product of transfer functions along ith forward path from input to output
Forward path determinant | Δi = Δ after deleting all loops touching Fi (Δi = 1 if Fi touches all loops).
Loop path | A path that starts from one variable and back to the same variable.
Non-touching loops | Two loops that don’t share a common variable.
Gives the transfer function between two variables in a much easier way than block diagram reduction.

## Slide 17: Example: Find transfer function C/R.
L2 and L3 are not touching (they do not have common variable).
F1 touches all loops.